## Slide 1: JAR/FAR 21
JAR/FAR 21 contains the ‘Certification Procedures for Aircraft and Related Products and
Parts’ for JAA and FAA certification respectively. JAR 21 deals with:
1 Procedural requirements for the issue of type certificates and changes to those certificates, the issue of standard certificates of airworthiness
2 Procedural requirements for the approval of certain parts
3 Procedural requirements for the approval of organizations related to the subject of the previous points.
4 Rules governing the holders of any certificate or approval specified in the previous points.

## Slide 2: In a similar way, FAR 21 deals with: 1 Procedural requirements for the issue of type certificates and changes to those certificates, the issue of production certificates, the issue of airworthiness certificates 2 Rules governing the holders of any certificate 3 Procedural requirements for the approval of certain materials, parts, processes

## Slide 3: EASA Part 21
As we previously mentioned, this document replaces JAR 21, which remains the core of the same document. The changes to the JAR document reflect the new legal status of the EASA towards the national authorities and a full revision of the document in light of the JAA certification experience.
Type certificates
Subpart H of Part 21 (Article 21A.184) includes the ‘Restricted type certificates’ missing in JAR 21.

## Slide 4
Airworthiness certificates
Subpart H of Part 21 (Article 21A.173) classifies the airworthiness certificates as follows:
1 A certificate of airworthiness shall be issued to aircraft which conform to a type certificate that has been issued in accordance with this Part.
2 Restricted certificates of airworthiness shall be issued to aircraft:
(a) that conform to a Restricted type certificate that has been issued in accordance with this Part, or
(b) that have been shown to the Agency to comply with specific certification specifications ensuring adequate safety
3 Permits to fly shall be issued to aircraft that do not meet, or have not been shown to meet, applicable certification specifications but are capable of safe flight under defined conditions.

## Slide 5
The certificates in 1 are equivalent to the Standard certificates of airworthiness of JAR 2.
The certificates in 2 are consequent to the Restricted type certificates and do not exist in
JAR 21.
The certificates in 3 have the characteristics of the Special certificates of airworthiness currently issued by national authorities and are not included in JAR 21
Environmental protection
Part 21 of the type certification includes the designation of applicable environmental protection requirements and certification specifications, missing in JAR 21.

## Slide 6
Structure of aircraft airworthiness standards
If we look at the airworthiness standards for aircraft certification (JAR/CS-22, JAR/CS-VLA,
JAR/CS-VLR, JAR/FAR/CS-23, -25, -27, and -29), we note a common structure that entails a certain unity and uniformity.
Apart from the forewords, the lists of pages, etc., we find ‘subparts’
and ‘appendices’. As mentioned previously, the JARs/CS also contain advisory material.
Each subpart contains paragraphs under a title (e.g. ‘Ground Loads’, ‘Control Systems’, etc.), and it is of interest to see that, in all the above standards, the same topics are generally dealt with in paragraphs bearing the same number (e.g. ‘Weight limits’ paragraph XX.25; ‘Materials and workmanship’ paragraph XX.603; etc.). This makes it easier to pass from one standard to another, and to define comparisons when that is needed.

## Slide 7
Some details of this structure are as follows:
1 Subpart A: General. This Subpart provides information about the types and categories of aircraft to which the standard is applicable.
2 Subpart B: Flight. This Subpart deals with the flight tests to be carried out to show compliance with the requirements for performance, controllability and maneuverability, stability, etc. It is worth stating that this Subpart does not exclusively cover certification flight tests; other Subparts contain some requirements that must be complied with through flight tests.
3 Subpart C: Structure. This Subpart contains the requirements for flight and ground load assessment, and for structural design of airframes, control systems, landing gears, and other components. Crashworthiness and fatigue requirement parameters are also provided.

## Slide 8
4 Subpart D: Design and Construction. This Subpart deals with the design technique, materials, safety factors, control system and landing gear design, structural tests to be carried out, cockpit and passenger cabin design, fire protection and flutter requirements, etc.
5 Subpart E: Power Plant. This Subpart contains the requirements for power plant installations and related systems (like fuel, oil, exhaust systems, etc.). Power plant controls, accessories, and fire protection are also considered.
6 Subpart G: Operating Limitations and Information. This Subpart provides requirements for all the information that must be available to the pilot and other personnel for correct aircraft operations: from marking and placards, to the flight manual content.
7 Appendices. These documents are of various natures; they can provide simplified design load criteria, test procedures for assessment of material flammability, instructions for continued airworthiness, and other information.

## Slide 9: Aircraft airworthiness standard applicability
JAR/CS-22. Sailplanes (glider) and Powered Sailplanes
1 Sailplanes with a maximum weight not exceeding 750 kg.
2 Single-engine (spark or compression ignition) powered sailplanes with a design value W/b2 (weight to span2) not greater than 3 (W in kg, b in m), and maximum weight not exceeding 850 kg.
The maximum number of occupants for both sailplanes and powered sailplanes must not exceed two.

## Slide 10
JAR/CS-VLA. Very Light Aeroplanes
This includes aeroplanes with a single engine (spark or compression ignition) having no more than two seats, with a maximum certificated take-off weight of not more than 750 kg and a stalling speed in the landing configuration of not more than 45 knots (CAS). The approval to be given must be for day-VFR51 only.
In the United States, where the requirements have been adopted the VLA certification for night flight and IFR52 is possible, in compliance with the additional
requirements of AC 23–11. In Europe, this possibility has not yet been approved.

## Slide 11
JAR/FAR/CS-23. Normal, Utility, Aerobatic, and Commuter Category Aeroplanes
1 Aeroplanes in the Normal, Utility, and Aerobatic categories that have a seating configuration, excluding the pilot seat(s), of nine or fewer and a maximum certificated take-off weight of 5670 kg (12 500 lb) or less.
2 Propeller-driven, twin-engine aeroplanes in the Commuter category that have a seating configuration, excluding the pilot seat(s), of 19 or fewer and a maximum certificated takeoff weight of 8618 kg (19 000 lb) or less.

## Slide 12
JAR/CS-25. Large Aeroplanes/FAR 25. Transport Category Airplanes
These comprise:
Large turbine-powered aeroplanes (JAA/EASA)
Transport category airplanes (FAA).
Note. There are no limitations as regards weight, number of engines, and number of occupants.

## Slide 13
JAR/CS-27. Small Rotorcraft/FAR 27.
Normal Category Rotorcraft
Rotorcraft with a maximum weight of 3175 kg (7000 lb) or less and nine or less passenger seats.
Multi-engine rotorcraft may be type certificated as Category A provided the requirements referenced in Appendix C are met.
Note. For Category A definition, see the Notes on JAR/FAR/CS-29.

## Slide 14
JAR/CS-29. Large Rotorcraft/FAR 29. Transport Category Rotorcraft
Rotorcraft categories are as follows:
1 Rotorcraft must be certificated in accordance with either the Category A or Category B requirements of JAR/FAR/CS-29. A multi-engine rotorcraft may be certificated as both
Category A and Category B, with appropriate and different operating limitations for each
category.
2 Rotorcraft with a maximum weight greater than 9072 kg (20 000 lb) and 10 or more
passenger seats must be type certificated as Category A rotorcraft.
3 Rotorcraft with a maximum weight greater than 9072 kg (20 000 lb) and nine or less
passenger seats may be type certificated as Category B rotorcraft provided the Category
A requirements of Subparts C, D, E, and F of JAR/FAR/CS-29 are met.

## Slide 15
FAR 31. Manned Free Balloons
1 Captive gas balloons deriving lift from a captive lighter-than-air gas.
2 Hot-air balloons deriving lift from heated air.
Notes. There are no limitations on weight and number of occupants. The certification maximum
weight is the highest weight at which compliance with each applicable requirement of
this part is shown.

## Slide 16
JAR/CS-VLR. Very Light Rotorcraft
Very light rotorcraft with a single engine (spark or compression ignition) having no more than two seats, with a maximum certificated take-off weight of not more than 600 kg. The approval
has to be for day-VFR only.

## Slide 17
Airworthiness standards for unmanned aircraft
These aircraft are internationally known as Unmanned Aerial Vehicles (UAVs) or Uninhabited Aerial Vehicles (UAVs), and also as Remotely Piloted Vehicles (RPVs) and
Remotely Operated Aircraft (ROAs).
We should not be misled by the title: at the time of writing (July 2005), no official airworthiness standards for UAVs exist.

## Slide 19
Two main parts of airworthiness is:
Ground tests
Flight test

## Slide 25
STRESS
STRAIN
Poisson’s Ratio Effect
Shear Strain
Strain Rate
Elongation and Reduction of Area
TENSILE PROPERTIES
Modulus of Elasticity (E)
Tensile Proportional Limit Stress (Ftp)
Tensile Yield Stress (TYS or Fty)
Tensile Ultimate Stress (TUS or Fty)

## Slide 27
COMPRESSIVE PROPERTIES
Compressive Ultimate Stress (Fcu)
Compressive Yield Stress (CYS or Fcy)
SHEAR PROPERTIES
Modulus of Rigidity (G)
Proportional Limit Stress in Shear (Fsp)
Yield and Ultimate Stresses in Shear (SYS or Fsy) and (SUS or Fsu)
BEARING PROPERTIES
Bearing Yield and Ultimate Stresses (BYS or Fbry) and (BUS or Fbru)

## Slide 28
TEMPERATURE EFFECTS
Low Temperature
Temperatures below room temperature generally cause an increase in strength properties of metallic alloys. Ductility, fracture toughness, and elongation usually
decrease. For specific information, see the applicable chapter and references noted therein.
Elevated Temperature
Temperatures above room temperature usually cause a decrease in the strength properties of metallic alloys. This decrease is dependent on many factors, such
as temperature and the time of exposure which may degrade the heat treatment condition, or cause a metallurgical change. Ductility may increase or decrease with increasing temperature depending on the same variables.

## Slide 29
Creep and Stress-Rupture Properties

## Slide 30: الزامات مواد وعناصر فلزی برای سازه­های وسایل نقلیۀ هوا فضایی

## Slide 34
راستایاصلیa آزمايش براي آلياژهاي مختلف
a: اگرچه به جهت تعیين خواص مكانيكي، مي­بايست اين خواص در دو يا سه راستای دانه­بندی تعيين شوند،
راستای اوليۀ تست همان راستایی است كه بطور معمول مورد استفاده قرار مي­گيرد.
b: به ويژه­گي­هاي مكانيكي قابل كاربرد مراجعه شود.

## Slide 35
اطلاعات انتشارترک خستگي ممکن است از طریق چند نوع نمونۀ آزمایش مکانیک شکست، همانطور که در ASTM E647 توصیف شده است،بدست آيد. دو معیار اصلی برای پذیرش اطلاعات بدست آمده وجود دارد. یک معیار این است که یک فرمول معتبربرای تعيين ضريب شدت تنش در نمونه، موجود باشد؛ معیار دیگر این است که تنش­های خالصبدست آمده از طریق روابطاوليۀمقاومت مصالح، کمتر از هشتاد درصد (80%)استحکام تسلیم کششي مواد باشد.
Stress intensity factor

## Slide 36: در آزمایشات، اطلاعات اصلی مانند طول­های ترک، a، و تعداد سيكل­هاي مرتبط با آنها، N، بدست مي آیند. مقادیر رشد-ترک بعنوان شیب­ها، یا متوسط شیب­ها در بخش­هاي مختلف منحني رسم شده از اطلاعات آزمايش، تفسیر می­شوند.

## Slide 37
منحني رشد ترك

## Slide 38
FATIGUE PROPERTIES

## Slide 39: اتصالات مکانیکی با پیچ و پرچ
مقاومت­های برشی از طریق آزمایش برش بحرانی در وضعیت برش تکی یا برش مضاعف تعیین خواهند شد. نتایج آزمایش برش مضاعفک ه مطابق باآزمایش شمارۀ13از استانداردNASM 1312، انجام شده، بر نتایج برش تکی ارجحیت دارد.

## Slide 40: اتصالات جوش­ذوبی