## Slide 1
Having already mentioned the standards as the technical documents issued to define design
criteria, we will now consider the ‘requirements’ (in the JAA terminology) or ‘regulations’
(in the FAA terminology): the obligatory standards.
Requirements, regulations, and standards

## Slide 2
The OSTIV,1 for example, publishes a standard for the design of sailplanes and powered sailplanes entitled ‘OSTIV Airworthiness Standard’. This document defines this organization’s vision on this subject.
However, if anyone applies for the certification of a sailplane in Europe, they must make reference to JAR 22,2 ‘Sailplanes and Powered Sailplanes’, because this is the only set of sailplane airworthiness standards with legal value, adopted by all JAA national authorities.
This means that the OSTIV Standard can only be a guide as well as a valuable reference point (also for the JAR 22 Study Group).

## Slide 3: JARs and FARs When the JAR requirements were first issued in the 1970s, several different standards for aircraft certification were in force in different countries.

## Slide 4
Federal Aviation Regulations (FARs) issued
by the FAA, adopted in the United States
In the UK, the Civil Aviation Authority that in 1972 replaced the Air Registration Board (ARB)
made use of the British Civil Air Regulations (BCARs).
In France the Direction Générale de
l’Aviation Civile (DGAC) had the Régles AIR.
In Germany the Luftfahrt Bundesamt had its
own regulations for sailplanes.

## Slide 5
Finally, on 1 January 1992, the JARs became part of the regulations of the European
Community, assuming legal status in the Community Countries (all existing equivalent regulations had to be superseded).
At present, only JARs (now replaced by the EASA regulations, as we will see) and FARs (or derivative regulations) are in practical use.

## Slide 6
List of JARs and FARs directly or indirectly related to airworthiness certification
JAR 1/FAR 1. Definitions and Abbreviations
JAR 11. JAA Regulatory and Related Procedures

## Slide 7
FAR 11. General Rulemaking Procedure
This part applies to the issuance, amendment, and repeal of any regulation for which the FAA follows public rulemaking procedures under the Administrative Procedure Act (‘APA’).

## Slide 8
JAR 21. Certification Procedures for Aircraft and Related Products and Parts
FAR 21. Certification Procedures for Products and Parts
JAR 22. Sailplanes and Powered Sailplane
JAR-VLA. Very Light Aeroplanes
JAR 23. Normal, Utility, Aerobatic and Commuter Category
Aeroplanes
FAR 23. Airworthiness Standards: Normal, Utility, Acrobatic
and Commuter category airplanes

## Slide 9
JAR 25. Large Aeroplanes
FAR 25. Airworthiness Standards: Transport category airplanes
JAR 26. Additional Airworthiness Requirements for Operations
.

## Slide 10
JAR 27. Small Rotorcraft
FAR 27. Airworthiness Standards: Normal category rotorcraft
JAR 29. Large Rotorcraft
FAR 29. Airworthiness Standards: Transport category rotorcraft
FAR 31. Airworthiness Standards: Manned free balloons
JAR-E. Engines
This code is based on the English BCAR Section C and contains the airworthiness requirements for engines. Subsections B and C deal specifically with piston engines; subsections D and E deal specifically with turbine engines.
FAR 33. Airworthiness Standards: Aircraft engines
This part prescribes airworthiness standards for the issue of type certificates for aircraft engines and changes to those certificates. Subparts C and D deal specifically with reciprocating aircraft
engines; Subparts E and F deal specifically with turbine aircraft engines

## Slide 11
JAR-APU. Auxiliary Power Units
This code is based on FAA Technical Standard Order TSO-C77a and provides airworthiness requirements for the release of JTSO authorizations for turbine powered auxiliary power units for use on aircraft.
FAR 34. Fuel Venting and Exhaust Emission Requirements for Turbine Engine Powered Airplanes
The provisions of this subpart are applicable to all in-use aircraft gas turbine engines of the classes specified, certificated for operations within the United States.
As regards foreign airplanes, this FAR applies only to those foreign civil airplanes that, if registered in the United States, would be required by applicable Federal Aviation Regulations to have a US standard airworthiness certificate in order to conduct the operations intended for the airplane.

## Slide 12
JAR-P. Propellers
The requirements of this code apply to propellers of conventional design.
FAR 35. Airworthiness Standards: Propellers
This part prescribes airworthiness standards for the issue of type certificates and changes to those certificates for propellers.
JAR 36. Aircraft Noise
The applicable noise requirements for the publication of a type certificate for an aircraft are prescribed according to the provisions of Chapter 1 of ICAO Annex 16.

## Slide 13
FAR 36. Noise Standards: Aircraft type and airworthiness certification
FAR 39. Airworthiness Directives
The regulations in this part provide a legal framework for the FAA’s system of Airworthiness Directives.
FAR 43. Maintenance, Preventive Maintenance, Rebuilding, and Alterations
FAR 45. Identification and Registration Marking

## Slide 14
JAR-TSO. Joint Technical Standard Orders
While the requirements for issue of JTSOs are found in JAR 21 Subparts O and N–O, the code provides the list of JTSOs as follows:
Index 1: the JTSOs that are technically similar to FAA TSOs.
Index 2: the JTSOs that are applicable only to JAR (different from FAA TSOs, or corresponding FAA TSOs not existing).
A Technical Standard Order (TSO) is a minimum performance standard issued by the United States Federal Aviation Administration for specified materials, parts, processes, and appliances used on civil aircraft.

## Slide 15
JAR-OPS 1. Commercial Air Transportation (Aeroplanes)
This code prescribes requirements applicable to operation of any civil aeroplane for the purpose of commercial air transportation by any operator whose principal place of business is in a JAA Member State, with exceptions indicated in the same code.

## Slide 16
JAR-OPS 3. Commercial Air Transportation (Helicopters)
This code prescribes requirements applicable to any civil helicopter for the purpose of commercial air transportation by any operator whose principal place of business is in a JAA Member State, with exceptions indicated in the same code.

## Slide 17
FAR 91. General Operating and Flight Rules
FAR 101. Moored Balloons, Kites, Unmanned Rockets, and Free Balloons
FAR 103. Ultralight Vehicles
FAR 119. Certification: Air Carriers and Commercial Operators

## Slide 18
FAR 121. Operating Requirements: Domestic, flag, and supplemental operations
This part prescribes rules governing (in particular):
1 The domestic, flag, and operations of each person who holds an Air Carrier Certificate or Operating Certificate under FAR 119.
2 Each person employed or used by a certificate holder conducting operations under this part, including maintenance, preventive maintenance, and alteration of aircraft.

## Slide 19
FAR 125. Certification and Operations:
Airplanes having a seating capacity of 20 or more passengers or a maximum payload capacity of 6000 pounds or more; and rules governing persons on board such aircraft
This part prescribes rules governing the operations of the above-mentioned US-registered civil airplanes when common carriage is not involved, unless they are required to be operated under FAR 121, 129, 135, or 137, and unless other cases described in this part are applicable.

## Slide 20
FAR 129. Operations: Foreign air carriers and foreign operators of US-registered aircraft engaged in common carriage
This part prescribes rules governing the operations within the Unites States of each foreign air carrier holding (defined) permits issued by the Civil Aeronautic Board of the US Department of Transportation.
FAR 133. Rotorcraft External-Load Operations
This part prescribes airworthiness and operating certification rules for rotorcraft used in the above-mentioned operations in the United States by anyone, with the exceptions defined in the same document.

## Slide 21
FAR 135. Operating Requirements:
Commuter and on-demand operations and rules governing persons on board such aircraft
This part prescribes rules governing the commuter or on-demand operations of each person who holds or is required to hold an Air Carrier Certificate or Operating Certificate under FAR 119 and relevant items.
FAR 137. Agricultural Aircraft Operations
This part prescribes rules governing agricultural operations within the United States and the issue of commercial and private agricultural aircraft operator certificates for those operations.

## Slide 22
FAR 145. Repair Stations
This part describes how to obtain a repair station certificate. This part also contains the rules a certificated repair station must follow relating to its performance of maintenance, preventive maintenance or alterations of an aircraft, airframe, aircraft engine, propeller, appliance, or component part to which FAR 43 applies. It also applies to any person who holds, or is required to hold, a repair station certificate issued under this part.
FAR 147. Aviation Maintenance Technician Schools
This part prescribes the requirements for issuing aviation maintenance technician school certificates and associated ratings and the general operating rules for the holders of those certificates and ratings.

## Slide 23
JAR-AWO. All Weather Operations
This code prescribes requirements for:
1 Automatic landing systems.
2 Airworthiness certification of aeroplanes for operations with decision heights of 60 m (200 ft)down to 30 m (100 ft) – Category 2 operations.
3 Airworthiness certification of aeroplanes for operations with decision height below 30m(100 ft) or no decision height – Category 3 operations.
4 Directional guidance for take-off in low visibility.
JAR/CS-VLR. Very Light Rotorcraft

## Slide 24
References for certification of parts of aircraft
1 Joint Technical Standard Order authorization (JTSO) (JAR 21 Subpart O).
2 Technical Standard Order (TSO) (FAA AC 20–110).
3 Joint Part Approval authorization (JPA) (JAR 21 Subpart P).
4 Part Manufacturer Approval (PMA) (FAR 21.303).
5 Military and industrial specifications.
6 Specifications written in the aircraft certification process.